Automated Processing
cron:
runs rmg_process every minute
appends stdout and stderr to /var/log/rmg/rmg_process.log (hard-coded in crontab)

rmg_process:
serially executes automated processing scripts
only allows one instance to run at a time
sources rmg_env
calls:	rmg_det_to_db, rmg_filter_auto, rmg_position_auto, rmg_track_auto

rmg_det_to_db:
reads .det files, calculates signal parameters, writes to est table, writes .est files,	moves .est files to .tar file
only allows one instance to run at a time
rmg_env variables:
RMG_SERVER_DET_DIR = /rmg_server/det_files
root directory for .det files to be processed
RMG_SERVER_DET_ARCHIVE = /rmg_server/archive/det_files
root directory for .det files to be stored as compressed .tar files after processing
RMG_SERVER_DET_QUARANTINE = /rmg_server/quarantine/det_files
root directory to store .det files which are unable to be processed
RMG_SERVER_EST_ARCHIVE = /rmg_server/archive/est_files
root directory for .est files to be stored after processing
RMG_DIRECTORY_THROTTLE = 20
number of minute folders per site to process per invocation
input data:
.det files stored as $RMG_SERVER_DET_DIR/sitename/YYYY/MM/DD/hh/mm/deploymentIDssuuuuuu.det
outer loop processing:
for every directory found at $RMG_SERVER_DET_DIR/
if there is an entry for sitename in site table
walk directory tree depth-first in alphabetical (and chronological) order and process the first $RMG_DIRECTORY_THROTTLE minute directories (leaf directories)
output data:
if .det file processing is successful
appends est data to est table, uses auto-incrementing ID
writes .est file to $RMG_SERVER_EST_ARCHIVE/sitename/YYYY/MM/DD/hh/mm/deploymentID.est
moves .det file to compressed .tar file $RMG_SERVER_DET_ARCHIVE/sitename/YYYY/MM/DD/hh/mm/sitename.YYYY.MM.DD.hh.mm.tar
if unsuccessful
move failed .det file to $RMG_SERVER_DET_QUARANTINE/sitename_YYYY.MM.DD.hh.mm/
processing statistics:
beginning_timestamp = NULL
  ending_timestamp = NULL
beginning_index = NULL
ending_index = NULL
number_records_input = total number of minute directories read
number_records_output = total number of est records written to est table

rmg_filter_auto:
performs interval estimation and est scoring based on expected pulse time
only allows one instance to run at a time
rmg_env variables:
RMG_EST_THROTTLE = 50000
number of est records to score in a given invocation
RMG_EST_SCORE_INTERVAL = 60
time window parameter for estimating the pulse interval, in seconds
RMG_EST_SCORE_NEIGHBORHOOD = 20
time window parameter for scoring corroborators
input data:
guaranteed to score est records with IDs greater than estscore cursor and less than or equal to estscore + $RMG_EST_THROTTLE (estIDrange)
scoring is done with all available est records for a given time range so older records are re-scored and records with IDs greater than estscore + $RMG_EST_THROTTLE will be scored but will be re-scored when they fall within estIDrange
outer loop processing:
for every deploymentID with est records with ID within estIDrange
generate a sorted list of that deploymentID est records' timestamp
generate list of time ranges containing contiguous time windows (RMG_EST_SCORE_INTERVAL) which contain a timestamp from that list
for every time range run qraat.srv.signal.Filter()
splits data into non-overlapping score intervals starting at times evenly divisible by RMG_EST_SCORE_INTERVAL
estimates the transmitter period over that time
scores the est records in that interval based on records within +/- RMG_EST_SCORE_NEIGHBORHOOD / 2 of that record
output data:
interval estimates in estinterval table:
deploymentID, siteID, timestamp (start of interval window), duration (length of interval window), pulse_interval (average time between pulses), pulse_variation (standard deviation of time between pulses)
one interval estimate per deploymentID per siteID per time
old data is deleted
new data is appended with increasing ID
est scores in estscore table:
estID, score, theoretical_score (score if all pulses were present), max_score (highest score in interval window, <= theoretical_score)
one score per estID
old data is deleted
new data is inserted with same estID
!!No indication of processing order / reprocessed status!!
processing statistics:
beginning_timestamp = NULL
  ending_timestamp = NULL
beginning_index = estscore cursor + 1
ending_index = estscore cursor + RMG_EST_THROTTLE
number_records_input = total number of est records selected
number_records_output = total number of est records scored

rmg_position_auto:
performs bearing and position estimation of scored est records
only allows one instance to run at a time
rmg_env variables:
RMG_POS_EST_THRESHOLD = 0
scoring threshold for est records to pass filter
RMG_POS_TIME_WINDOW = 30
time window, in seconds, over which to average est records into bearings and positions
RMG_POS_TIME_STEP = 15
time step, in seconds, to advance the time window
input data:
guaranteed to determine bearing and position estimations for est records with ID greater than position cursor and less than estscore cursor which have score / theoretical_score > RMG_POS_EST_THRESHOLD in the estscore table (filtered_estIDs)
outer loop processing:
for every deploymentID with est records with ID in filtered_estIDs
generate a sorted list of that deploymentID filtered_estIDs' timestamp
generate list of time ranges containing contiguous time windows
for every time range run qraat.srv.position.estimator
output data:
bearing estimates in bearing table:
deploymentID, siteID, timestamp, bearing, likelihood, activity, number_est_used
new records are appended to table with new IDs
there can be records with the same deploymentID, siteID, and timestamp
position estimates in position table:
deploymentID, timestamp, latitude, longitude, easting, northing, utm_zone_number, utm_zone_letter, likelihood, activity, number_est_used
new records are appended to table with new IDs
there can be records with the same deploymentID and timestamp
processing statistics:
beginning_timestamp = NULL
  ending_timestamp = NULL
beginning_index = position cursor + 1
ending_index = max estID processed
number_records_input = total number of est records in filtered_estIDs
number_records_output = total number of positions inserted

rmg_track_auto:
performs track filtering of new position estimates
only allows one instance to run at a time
rmg_env variables:
None, !!needs hard-coded variables moved to rmg_env!!
input data:
positions which have an ID > track_pos cursor
outer loop processing:
for every deploymentID with positions with ID > track_pos cursor
for each non-overlapping 4 hour (hard-coded) time window with such position record
determine the independent track during this window
output data:
track_pos table
ID, positionID, deploymentID, timestamp
delete all records with timestamp over calculated window
append positions that belong to the calculated track
processing statistics:
beginning_timestamp = NULL
  ending_timestamp = NULL
beginning_index = track_pos cursor
ending_index = maximum index included in a track
number_records_input = number of positions with ID > track_pos cursor
number_records_output = number of positions written to track_pos table